## Slide 1
Procedure to solve
Circuit
A presentation on methods and procedures to solve a series or a parallel electrical circuit.

## Slide 2
Introduction of Series Circuit

## Slide 3: What is circuit?
A circuit is a closed loop that electrons can travel in. A source of electricity such as a battery provides electrical energy in the circuit.

## Slide 4: Types of Circuit
Series circuit
Parallel circuit

## Slide 5: Series circuit
The components are connected end- to- end, one after another. They make a simple loop for the current to flow round. The total resistance R,
R=R1 +R2+R3

## Slide 6: Series circuit
Current is the same at all points in the circuit
Voltage is shared between the components

## Slide 7: Series circuit
One path(s) for current
Adding resistance in series decreases total current
Decreased current means dimmer light
Break in circuit stops all current

## Slide 8
Structure of Series Circuit

## Slide 9: Component of a circuit
A circuit needs three thing:
1. Energy Source
2.Path(wire)
3.Load( light & resistance etc.) 4. key / switch

## Slide 10: How to work circuit by Ohm’s Law
Most problems involve three characteristics of a circuit:
i) resistance R,
ii) voltage V and
iii) current I
Ohm's Law tells that they are related in a simple way:
V = IR.
I = V / R
R = V/I

## Slide 11: How to work current in series circuit
In a series circuit :
i. only one path for current flow,
ii. following same current at all points on the circuit

## Slide 12: Character of voltage in series circuit
Dropping the voltage across each component of the series circuit add up to the total voltage drop across the circuit like:
v1 + v2 + v3 = Vt (total voltage)
It is Called kirchhoff’s voltage law ( KVL)

## Slide 13
Solving a Series Circuit

## Slide 14: Solving a Series Circuit
Kirchhoff’s Voltage law(KVL): The algebraic sum of all voltages around a closed loop must be equal to zero. Σ voltage drops - Σ voltage rises = 0 or, Σ voltage drops = Σ voltage rises
The sum of all the voltages around the loop is equal to zero : v1+v2+v3-v4=0.

## Slide 15: Solving a Series Circuit
RTotal = 12Ω.
According to ohm’s law: V=IR.
So, Is = 1.67A
vD = V1+V2+V3
= IsR1+IsR2+IsR3
= 20.04V
So, here voltage drops and voltage rises are same. The sum of all the voltages around the loop is equal to zero.

## Slide 16
Introduction of Parallel Circuit

## Slide 17: Parallel Circuit

## Slide 18: Advantages & Usage of parallel circuit
Equipments gets same power.
Individual switching system.
Easy replacement.
Used in household wiring.
Shunt is connected in parallel circuit.